LED PANEL LIGHT

Item No.:ES-PL-R2413

SPECIFICATION

LED Panel Light

Features:

- Super-thin, super-light and super-brightness.

- New design of optical configuration with high brightness, equal emitting surface, no flare, no flash and high efficiency for energy saving.

- Adapting current circuit design with stable working, reliable effect.

- Using optical panel material to improve the efficiency of light.  High-thermal conductivity aluminum alloy to improve the efficiency of heat conduction.

- Perfect quality SMD, LED as light source with high light efficiency, speed activate, long lifetime.

- No noise and flash when working and frequent activation no affect light source.

- Warm white, natural white and cool white for choosing according to customer’s requirements.

- Beautiful, super- light design, and convenient installation.

- Long-life using can lower maintain cost.

- Different installation for choosing as customer’s requested.

LED panel light specifications:

| LED PANEL SPECIFICATIONS |
| --- |
| NUMBER | ITEM | DESCRIPTION |
| 1 | Input voltage | AC 100~240V |
| 2 | Panel Input | DC:12-48V，Constant Current:0.35A |
| 3 | Power consumption | 16W |
| 4 | luminous flux | 1124lm |
| 5 | Color | White |
| 6 | Color temperature | 3000-6000K |
| 7 | Life time | >50,000 Hour |
| 8 | Operating temperature | -20ºC to + 50ºC |
| 9 | Storage temperature | -30ºC to + 60ºC |
| 10 | Certificates | CE RoHS FCC |
| 11 | Size | Diameter:240.0mm |
| 12 | Protection Grade | IP20 |

Panel Size:

Light Distribution Graph

Average Illuminance Figure

Electrical connection diagram:

Installation:

1. Built-in installation

- Make a hole in the wall or the ceiling,the diameter of the hole is 225-230mm

- Connect  the  Power  Supply  Cable.

- Carefully make the clamp spring  and round panel into vertical state and put the clamp spring in the hole,then round panel close to the wall and ceiling

A，

B，

Package

| 10boxs/Carton (1pc in a inner box) |
| --- |
| Quantity pcs | each piece in inner box and 10 pcs/carton |
| Weight KG | 8.9 |
| Inner box mm | 395x275x50 |
| Out carton mm | 562x407x268 |

Inner box package:

Outer Carton Package:

Attention

- Please be gentle when take out the product, in order to prevent scratch the surface.

- Please stay away from fire or high temperature object when product installation.

- Please turn off  the power before clean the lighting use dry dishcloth to wipe.

- Power supply, controller, tieline etc, to support our company's product, don't match others model.

- Let the children away from the product.

- When install or use the product meet the problem,pls ask the professional to maintain it and don't take apart the product without authorization.